# Example configuration
The LAN is considered DHCP powered and the TP-Link is OpenWRT powered.
This configuration is for two tagged VLANs to isolate two SSIDs.
--- 8< --- /etc/config/network
...
config interface 'lan'
        option ifname 'eth0'
        option proto 'dhcp'
        option hostname 'tp-link-coworkers'
config interface 'vlan101'
        option type 'bridge'
        option _orig_ifname 'eth0.101'
        option _orig_bridge 'true'
        option proto 'dhcp'
        option ifname 'eth0.101'
config interface 'vlan102'
        option type 'bridge'
        option _orig_ifname 'eth0.102'
        option _orig_bridge 'true'
        option proto 'dhcp'
        option ifname 'eth0.102'
...
--- >8 ---
--- 8< --- /etc/config/wireless
...
config wifi-iface
        option device 'radio0'
        option mode 'ap'
        option ssid 'La Bo[a]te Coworkers'
        option encryption 'psk2'
        option key 'xx'
        option network 'vlan101'
config wifi-iface
        option device 'radio0'
        option mode 'ap'
        option ssid 'La Bo[a]te Public'
        option encryption 'psk2'
        option key 'xx'
        option network 'vlan102'
...
--- >8 ---